## Slide 1: CSC258 – Project
Snake
By Darwin and Hongyu

## Slide 2: Snake Drawing FSM
First load initial positions of the Snake into the RAM in the form {x, y}
Draw from the RAM the current positions iterating through the first (length) positions
Update the position of the HEAD based on the direction the user has currently selected
Draw the new HEAD
Erase the previous position of the TAIL by drawing over it with black

## Slide 4: Game State FSM
Determines what is drawn on the screen
Transitions on user input / losing
Title and Game Over screen are bmp images
Animation is done by determining which ram
to read from inside the Datapath module
Title
Game
Game Over

## Slide 6: Problems We Ran Into
Understanding how to properly load and draw our stored values from the RAM, the address was being displayed one clock cycle too late
  In order to fix this we implemented wait states to load the addresses before trying to read from the address in the RAM
Trying to load .bmp files and drawing them on the screen, the pictures were being draw much differently then we expected
  This was an issue because the way we implemented the coordinates of the Snake initially was by concatenating the values of x and y and storing it in some address of the RAM, however the values were actually stored as the absolute pixel number

## Slide 7: Summary Table
Hongyu | Darwin
Snake FSM Snake Datapath Food drawing mechanics High score system | Game State FSM Game State Datapath Snake Datapath